-DISKBUG- Diskette Debugger for CP/M 8" Single Density Disks Page 1



                  Note  that  you  may do anything  you  want  with  this 
             program except sell it. Give it away to anyone who wants it, 
             and drop me a message with any bugs, suggestions etc. at the 
             NECS CBBS or thereabouts.

                  By   Tom Jennings
                       221 W. Springfield St.
                       Boston MA 02118

                  DISKBUG is a CP/M 1.4, 2.0, 2.2 or PDOS 1.17-up utility 
             that  provides read/write access to any sector or sectors of 
             an  IBM 3741 format diskette.  See a later section  for  use 
             with  other  formats.  DISKBUG  was originally  a  hack  for 
             installing  a  bootable CP/M system to a diskette,  but  has 
             grown  somewhat,  so  have patience with  the  poor  command 
             structure.

                  There are three logical entities in DISKBUG: the sector 
             oriented  commands,  the  file oriented  commands,  and  the 
             buffer.  

             BUFFER:
                  All  data is transferred through  the  buffer,  whether 
             to/from sectors or files. Data can be moved from one or more 
             sectors to a normal CP/M disk file,  or vice versa.  Data in 
             the buffer can be displayed or modified manually, similar to 
             DDT.

             SECTOR COMMANDS:
                  The  sector  oriented commands are all done via  direct 
             BIOS calls in CP/M,  or by system calls under PDOS.  One  or 
             more  sectors can be read at a time,  and multiple reads  or 
             writes  can extend over a track boundary;  for example,  you 
             can read two sequential sectors, starting at the last sector 
             in a track.

                  See the end of this manual for tips on using DISKBUG on 
             other diskette formats.

             FILE COMMANDS:
                  DISKBUG has a two file oriented commands.  These read a 
             disk  file into the buffer,  or write the buffer to  a  CP/M 
             disk  file.  Under PDOS,  the full filename spec can be used 
             (i.e.  FILE.NAME[99]  )  Character case conversion  is  done 
             automatically.











                                        1





        -DISKBUG- Diskette Debugger for CP/M 8" Single Density Disks Page 2



                                  DISKBUG OPERATION

                  DISKBUG  is  just a CP/M utility,  run  in  the  normal 
             manner.  It uses only 8080 opcodes, so will run on anything. 
             (Well,  anything we care about. Shows my narrow CPM-8080-Z80 
             point  of view) It is not particularly fast,  but who  cares 
             anyways. It does not use any command line arguments.

                  All  commands  are  quit  low  level,   which  I  found 
             appropriate for my uses,  such as system  installation,  un-
             erasing  files,  copying  files from Intel ISIS  and  PDP-11 
             diskettes.

                  One note on the buffer. It is assumed you have a fairly 
             large memory,  like 48K or so. The buffer is fixed at 32K in 
             length,  and almost no commands do any checking on  reaching 
             the  end  of it,  so it is possible to destroy  your  system 
             memory if you try. In practice, I have had no problems.

                  Buffer  management  is minimal.  All  commands  (except 
             display buffer and change buffer) operate from the bottom of 
             the buffer up.

                  The  command  prompt  always  displays  the  number  of 
             (decimal) bytes in the buffer.  All number typed to  DISKBUG 
             are in hex.

                  See the end of the manual for some examples.

                  A  hopefully  complete description of the  command  set 
             follows, with a list of features, bugs and side effects.

























                                        2





        -DISKBUG- Diskette Debugger for CP/M 8" Single Density Disks Page 3



                                 DISKBUG COMMAND SET

             X         Select the disk to use,
             R         Read sectors into the buffer,
             W         Write the buffer to sectors,
             G         Get a CP/M disk file,
             P         Put the buffer to a CP/M disk file,
             D         Display buffer contents,
             C         Change buffer contents,
             Q         Quit back to CP/M.


             X    -Select a disk drive.

                  This  command  must  be  performed  before  any  sector 
             command will operate. The disk selected will be used for all 
             upcoming  R or W commands.  Note that this is independent of 
             the  disk  used  by  the  G  and  P  commands;   see   those 
             descriptions for details.

             R    -Read one or more sectors to the buffer.

                  You are prompted for the starting track and sector, and 
             number of sectors.  All values are in hex.  Sectors are read 
             sequentially (assuming a standard diskette) into the buffer, 
             starting  at the bottom of the buffer.  Note that you cannot 
             append to data already in the buffer;  it gets  overwritten. 
             (If you need to,  you'll have to P it out to a diskfile, and 
             append it later manually.)

                  Note  that  no checking is done on the amount  of  data 
             read;  if  you  specify  more than  128  sectors,  you  will 
             probably bash something.

             W    -Write buffer data out to one or more sectors.

                  As in the R command,  you are prompted for the starting 
             track and sector, and number of sectors. To be safe, it asks 
             "Write  to  disk <x>:?" before actually  writing,  therefore 
             allowing you to abort.

                  Only  the  specified  number  of  sectors  is  written, 
             regardless of how much data is in the buffer. (even none!) 

             G    -Get a diskfile, put it in the buffer.

                  This reads the specified disk file and puts it into the 
             buffer,  starting  at the bottom of the buffer.  The  entire 
             file  is  read  until end of file.  Note that you  can  (and 
             probably should!) specify a disk other than the one selected 
             by  the X command.  File names are specified as  per  normal 
             operating system specs:  X:FILE.NAM, or with the user number 
             if PDOS. All characters are converted to upper case.



                                        3





        -DISKBUG- Diskette Debugger for CP/M 8" Single Density Disks Page 4


             P    -Put the buffer contents to a diskfile.

                  All  data  within  the buffer is written to  the  disk. 
             NEVER  'P'  to the same disk as selected by the  X  command, 
             unless you were merely reading from it.  Filenames are  full 
             legal names, as described above. The number of bytes written 
             out is the same as listed at the prompt.

             D    -Display buffer contents.

                  D  prompts  you  for a  buffer  starting  address,  and 
             displays  256  bytes in hex and ASCII.  This address is  the 
             offset  from  the start of the buffer,  and runs from  0  to 
             7f00.   Unfortunately,  you  have  to  maintain  the  buffer 
             address/sector numbers yourself.  For example,  if you  have 
             read  4 sectors from track 0 sector 10,  sector 10 is in the 
             buffer at 0 to 7f, sector 11 at 80 to ff, etc.

                  You  may type CR only at the address prompt to  display 
             the next sequential 256 bytes instead of the next address.

             C    -Change buffer contents.

                  This command is patterned after Digital Research's  DDT 
             'S'  command.   After  entering  the  address,  the  current 
             contents are displayed,  and you can enter new ones. Type an 
             illegal  hex  number to quit.  CAUTION:  Unlike  DDT's  'S', 
             typing  CR  only  as  new contents will  wreck  the  current 
             contents,  not leave it.  You MUST retype the same value  if 
             you want to leave it alone.

             Q    -Quit back to the operating system.

                  Pretty  much self explanatory.  Does absolutely nothing 
             to the X'd disk, the buffer, or any diskfiles.






















                                        4





        -DISKBUG- Diskette Debugger for CP/M 8" Single Density Disks Page 5



                   NOTE ON OPERATING ON OTHER TYPE DISKETTE FORMATS

                  Although  DISKBUG  is meant for use  only  on  standard 
             eight inch single density disks,  you can use it on any type 
             diskette  if  you DO NOT attempt to perform multiple  sector 
             I/O  the would make DISKBUG think it should  change  tracks, 
             and  make certain concessions.  Track size is currently hard 
             coded to 26 sectors per track.  (Someday I'll finish DISKBUG 
             so it reads the CP/M disk descriptor block...)

                  When a sector write is done,  a "write allocated"  type 
             write is done.  If you write to a diskette that has physical 
             sectors  larger  than  128  bytes,  before  you  remove  the 
             diskette  make  sure  you perform some operation  that  will 
             ensure  the sector actually gets written;  reading a  sector 
             will do.

                                       EXAMPLES

                  Here are some simple examples to show various things.

                   READ THE CP/M SYSTEM TRACKS, DUMP TO A DISK FILE

                  This  is one of the simplest things to do.  Select  the 
             disk  to  read,  say A:,  using the X  command.  Do  an  'R' 
             command,  and  read the first two tracks to the  buffer.  At 
             this  point,  you might poke around with the 'D' command  to 
             see  what's  there.   To  write  it  to  a  diskfile,   say, 
             TRACK2.BIN, so you can look at it with DDT or something, use 
             the 'P' command.  In this case,  you can 'P' it to disk  A:, 
             since you only read it.

             (0 bytes in buffer) pick one: X
             Disk: A

             (0 bytes in buffer) pick one: R
             Track: 2
             Sector: 1
             # sectors: 1A
             Disk IO complete

             (3322 bytes in buffer) pick one: D
             Starting address: 0

             0000: 31 80 00 44 1a 7c 55 66 77 88 aa 55 4f 3e 1a 3c 1__D_|Ufw__UO>_<
             0010: 41 42 43 44 45 31 32 33 34 35 61 62 63 64 65 66 ABCDE12345abcdef
             .... etc

             (3322 bytes in buffer) pick one: P
             File to write to: A:TRACK2.BIN

             (3322 bytes in buffer) pick one: Q
             A>



                                        5





        -DISKBUG- Diskette Debugger for CP/M 8" Single Density Disks Page 6




                     WRITING A DISKFILE OUT TO THE SYSTEM TRACKS

                  This  was  the  original  use  of  DISKBUG.   Read  the 
             diskfile,  say SYSTEM.COM,  to tracks 0 and 1.  Note that in 
             this  example  the disk file is larger than the size of  the 
             two tracks,  like you SAVEd too many blocks.  However,  only 
             the desired 6144 bytes will be written out.

             (0 bytes in buffer) pick one: G
             File to read: A:SYSTEM.COM
             Buffer contains 8192 bytes         (I should delete this msg...)

             (8192 bytes in buffer) pick one: X
             Disk: B

             (8192 bytes in buffer) pick one: W
             Track: 0
             Sector: 1
             # sectors 33                       (did I add right?)
             Write to disk A:? Y
             Disk IO complete

             (8192 bytes in buffer) pick one:

                               UNDELETE A CP/M DISKFILE

                  First,  read track 2 into the buffer (r,2,1,1a) Use the 
             'D'  command to look for the directory entry  (below).  Once 
             found,  use the 'C' command to change the ET byte from E5 to 
             the desired user number (0 will do) If the file was over 16K 
             bytes,  don't  forget the other extents (same  filename,  EX 
             byte  1,2,3...  for each extent) In order to update the disk 
             directory, write the entire track back (w,2,1,1a) 






















                                        6





        -DISKBUG- Diskette Debugger for CP/M 8" Single Density Disks Page 7


                                 BUGS AND "FEATURES"

                  This  first  one is not a bug,  but an  undesired  side 
             effect  of fiddling with the BIOS without the  BDOS  knowing 
             it.  Bad  things  can  happen when you  change  the  default 
             disk,  and you aren't careful to specify the disk when using 
             the 'P' or 'G' commands. 

                  There  is  possibly  a bug in the  disk  select  stuff, 
             however. I couldn't get it to repeat, but I thought I should 
             mention it anyways.  After performing sector reads or writes 
             to a disk, a file access, such as 'G' or 'P' may look on the 
             wrong  disk.  Fortunately,  this happened only with the  'G' 
             command  ("Can't find FILE.NAM") and was not destructive.  I 
             really should add a DISK SELECT command via a BDOS call.

                  The number and filename parsers aren't too smart.  They 
             will not report errors such as illegal hex numbers, or blank 
             filenames. Be careful here.

                  If  you read a file greater than 32K  bytes,  you  will 
             probably munch something.

                  In the 'C' command, typing CR in response to the prompt 
             for a new value will not leave that location alone, but will 
             change it to some random value.

                  If  you  write an empty buffer to a diskfile,  it  will 
             create a file with one (garbage) byte in it.

                               ---- End of Manual ----


























                                        7